## Slide 1: Ultra Low Power PLL Implementations
Sudhanshu Khanna
ECE7332 2011

## Slide 2: Motivation for ULP PLLs
Distributed systems:
  Wireless Sensor Networks
  Body Sensor Networks
Individual nodes are simple and rely on communication to hub for getting the work done
Must adhere to standard wireless communication protocols => PLL for RF Communication
To generate clock(s) for the digital system
  => PLL for processing

## Slide 3: Outline
ULP PLL for RF
  An Ultra-low-Power Quadrature PLL in 130nm CMOS for Impulse Radio Receivers
  200uW, 600MHz
ULP PLL for digital system clock generation
  Ultra Low Power CMOS PLL Clock Synthesizer for Wireless Sensor Nodes
  20uW, 100kHz
ULP ADPLL for RF
  260uW, 1GHz
  Duty cycled: On for 10% of the time

## Slide 4: ULP Quadrature PLL for Impulse Radio Receivers
For generating quadrature clocks for RF receiver
Specifications:
  Low power ~ 200uW
  600MHz output frequency
  -90 dBc/Hz @ 1MHz offset
Above specifications come from system level simulations

## Slide 5: ULP PLL for RF
Make sure your communication scheme and the architecture of the transceiver is such that the accuracy of the clock needed is low
Paper talks about how to do so, but will not focus on that
PLL Design Metrics
  Power is MOST important
  Since it is RF clock, phase noise is also given SOME importance
  No other metrics is given importance

## Slide 6: PLL Design
Differential Ring Oscillator based VCO
TSPC PFD
TSPC Divider
Low Noise Charge Pump
Fully integrated passive components

## Slide 7: VCO Design Specs
Consumes the largest share of the power consumption, thus its power optimization is most important
VCO requirements:
  Low Power
  Moderate phase noise, frequency
  Fully Integrated
  Quadrature outputs required

## Slide 8: VCO Design Decisions
VCO requirements:
  Low Power
  Moderate phase noise, frequency
  Fully Integrated
  Quadrature outputs required
Requirements 1, 2, 3: Suggest use of ring oscillator (RO)
  On chip LC oscillator will have bad “Q” and require large power consumption and area
  Thus, RO is a good solution for our noise requirements
Requirement 4: Quadrature outputs needed for receiver. Thus, differential VCO is the only solution

## Slide 9: VCO Delay Cell
Combination of inverter and cross coupling transistors for differential operation
2 stages used

## Slide 10: VCO Delay Cell
Why this structure?
  Power: It burns no static power for control voltage generation
  Full swing outputs: Good phase noise
Want to avoid using current controlled VCO
  Thus, MOS capacitors are used to control frequency

## Slide 11: VCO Results
100uW @ 600MHz, 1.3V
  50% of total power consumption
Small tuning range
  Only 23%
  Limited because of use of MOS varactors

## Slide 12: Divider
No fractional-N divider to save power
8 to 1 divider is used
Divider is also quite power hungry in a PLL
  TSPC FF is used to save clock power
  TSPC Helps save area too
  Since frequency is relatively low, TSPC works well
Divider power
  24uW (around 10% of total power)

## Slide 13: PFD
TSPC is used to make the D-FFs in PFD as well
NOR gate that generates the reset signal has delay of 300ps, and helps overcome dead-zone
10uW in lock

## Slide 14: Charge Pump
Since the PLL generates the clock for RF, some effort is put to lower noise due to charge pump
53uW at Iref of 14.5uA (25% of total power)
  Discussion: Is this too high a price??

## Slide 15: Charge Pump
Output transistors of the CP are biased such that there would be some static power consumption when both UP and DOWN are OFF
  This static would help compensate for leakage, and thus lower the ripple at VCO input when the PLL is locked
Also, inputs are not connected to the last stage, thus clock feed-through will be lesser

## Slide 16: Results
200uW @ 1.3V, 130nm process
  VCO: 100uW
  Charge Pump: 50uW
  Divider: 25uW
  PFD: 10uW
600MHz output frequency, 75MHz input clock
23% tuning range
-91 dBc/Hz @ 1MHz offset
~300u x 200u: mostly loop filter passives
Block | Power (uW)
Charge Pump* | 0.3
Divider | 3.0
PFD | 1.8
VCO | 9.7
Total | 14.8
***My PLL***

## Slide 17: Loop Filter
No active filter used to save power
Passive Implementation
  MIM capacitor
  High R poly

## Slide 18: Outline
ULP PLL for RF
  An Ultra-low-Power Quadrature PLL in 130nm CMOS for Impulse Radio Receivers
  200uW, 600MHz
ULP PLL for digital system clock generation
  Ultra Low Power CMOS PLL Clock Synthesizer for Wireless Sensor Nodes
  20uW, 100kHz
ULP ADPLL for RF
  260uW, 1GHz
  Duty cycled: On for 10% of the time

## Slide 19: ULP PLL for digital clock generation
Used to generate a 100kHz system clock for running digital circuits
The applications requires:
  +/- 0.05% freq accuracy
  < 40uW power @ 3.3V in 0.6u technology
  1us period jitter (large!)
  Fully integrated
  32kHz input clock from oscillator
  Discussion: Where do all these numbers come from??
Unlike previous design, here power is the most critical metric BY FAR

## Slide 20: PLL Architecture
Fractional N divider not used to save power
  3 dividers used to get to the required freq
All blocks focus on simplicity and low power
Very similar to class designs for PS3!

## Slide 21: VCO Design Decisions
To lower power, design decisions for VCO are most important
The authors use a single ended current starved RO
  Ease of integration
  Low Power at moderate noise
Discussion: Why not use differential cell from previous paper?
  Lower tuning range
  More switching nodes??
  Don’t need quadrature outputs

## Slide 22: VCO Design
M2-M3 form the inverter
M1-M4 are current sources
Other devices help create appropriate control voltages
M7 ensures that when VCTRL is below Vt then RO is still oscillating at some minimum frequency
  Discussion: Why is this required??

## Slide 23: Discussion: VCO: Need for Fmin
At startup, without M7, RO will not oscillate
Thus gain will be very high near Vt
  Stability issues??
  My PLL doesn’t oscillate < Vt but it works fine….

## Slide 24: Charge Pump
Issues to take care of:
  Spurs due to current mismatch
  Charge injection/sharing while switching current on and off
M11 and M12 help match the PU and PD structures in the charge pump
  Helps match charge injection and charge sharing effects

## Slide 25: Dividers
3 dividers are used to get to the required ratio
Discussion: What are the disadvantages of having dividers in the clock forward path?

## Slide 26: Results
20uW at 3.3V
100kHz output, 32kHz input
+/- 13Hz freq accuracy
5ns (1-sigma) jitter
0.8mm2 in 0.6u technology

## Slide 27: Outline
ULP PLL for RF
  An Ultra-low-Power Quadrature PLL in 130nm CMOS for Impulse Radio Receivers
  200uW, 600MHz
ULP PLL for digital system clock generation
  Ultra Low Power CMOS PLL Clock Synthesizer for Wireless Sensor Nodes
  20uW, 100kHz
ULP ADPLL for RF
  260uW, 1GHz
  Duty cycled: On for 10% of the time

## Slide 28: ULP ADPLL for RF
Has 10% duty cycle
  Output clock is only available in bursts
  Duty cycling helps reduce average power
WSNs do not need very accurate RF clock:
  Because special transceiver architectures can be used that may tradeoff other metrics for clock accuracy
  0.25% freq error is enough
  However, free running, periodically calibrated VCO is still not good enough
Final PLL results:
  0.2x0.15mm2
  260uW @ 1.3V, 1GHz output clock

## Slide 29: Duty Cycled PLL
PLL runs in bursts
Corrects itself only during the idle time between bursts
Must have a fast startup DCO
  So that power hungry transient is small
  So that the output is available for the most part of the burst
DCO input is stored in between bursts
  Thus ADPLL is a must

## Slide 30: ADPLL architecture
Dual loops for course and fine tuning
Main (course) loop:
  DCO with 7-bit DAC, counter, accumulator, subtractor
  FCW = Desired Fo / Fref

## Slide 31: Course Acquisition
Every 1 out of 10 ref cycles, the ADPLL is “ON”
Counter counts the number of rising edges of Fo within one burst
1 burst = 1 ref cycle
After burst is over, subtractor calculates error between counter value and FCW
That freq error information is updated in the accumulator, and is used in the NEXT burst

## Slide 32: Course Locking
Once in lock:
  Successive bursts have same number of rising edges, except for effects of quantization error
  No course error except for quantization error
Quantization error can result in freq error as large as ref freq (i.e. 1 counter bit * input freq)

## Slide 33: Lower the quantization error
Quantization error obviously results in freq error
Large quantization error (QE), together with large loop gain can result is stability
  ADPLL will oscillate around the target freq
  Must design loop gain to be in stable across PVT
  Lower QE => lower loop gain => stability
How to lower QE:
  Higher resolution course acquisition
    More power hungry
    Must be always on
  Thus better to have 2 loops, course and fine

## Slide 34: Fine Acquisition Loop
Their ADPLL has 2 loops
  Course: With 7 bit DAC controlling the DCO
  Fine: With 9 bit DAC controlling the DCO
  Only one 16 bit loop can do, but its more area, power. Banking helps reduce these metrics.
Fine Loop:
  Subtractor
  BW control
  Accumulator
  9 bit DAC

## Slide 35: Fine Tuning
Course loop gives zero error if edges = FCW or FCW + 1
Once course tuning gives zero error, fine tuning makes sure that the (FCW+1)th edge comes as closer to the ref edge as possible
Fine tuning loop works in bang-bang fashion.
The last edge comes either just before or just after the ref clock edge

## Slide 36: Fine Loop Adaptive Control
Till course error is high, fine loop is OFF
Till fine error is high, fine loop BW is high
Saves power, decreases acquisition time

## Slide 37: DCO
Low power: Use VCO (not LC)
Fast startup
  Don’t use LC
  Large capacitors on control voltage nodes
  Control voltages set before DCO startup
  DCO configured as delay line before startup
  DAC turned off in between bursts

## Slide 38: Results
20MHz ref
300M-1.2GHz output
260uW @ 1.3V, 1GHz
  DCO: 100uW
  DAC: 60uW
  Counters, other digital logic: 40uW
Initial settling happens in ~15 bursts
Once settled DCW only changes bec of temp, voltage variations
Phase Noise: -77dbc/Hz @ 1MHz offset
< 0.25% frequency error

## Slide 39: Summary of best ULP practices
Use VCO with as less static current dissipation paths as possible
Varactor based cell is good if required tuning range is small
Make VCO fast startup, and duty cycle the PLL
Duty cycling may need PLL to be ADPLL
Use TSPC to lower power in dividers
Use elaborate CP only if clock is for RF